## Slide 1: Buckendale Lecture Transitioning commercial vehicles to zero impact emissions – Challenges and Opportunities ahead
Dr. Ameya Joshi
Date : September 21st, 2022
joshia@corning.com https://www.linkedin.com/in/joshiav/

## Slide 2: Acknowledgments
Julie Blumreiter (ClearFlameEngines)
Matt Fernley (Battery Materials Review)
Vivek Sujan (Oak Ridge Natl. Lab)
Beth Hinchee (Caterpillar)
Shakti Saurabh (Cummins)
Addie Majewski (DieselNet)
Mats Hultman (Neste)
Felipe Rodríguez (ICCT)
Roland Dauphin (Concawe)
Mark Herbst, Tom Waldron (SuperTurbo)
Chris Sharp (SWRI)
Special thanks to the Buckendale Committee for keeping me honest
(and hopefully on time !)
And to my boss, Dr. Willard Cutler, for his mentorship and freedom in working on these topics

## Slide 3: Perception : Electrification is the solution for transport decarbonization R&D spending and policies are skewed heavily towards ZEVs
ICE
Fuels
Electrification
Efficiency improvements
SuperTruck 55% BTE
Alternate fuels
CNG, LPG
ZEVs
Battery electrics
Fuel cell vehicles

## Slide 4: Opinion: We need to pursue all pathways for decarbonization - True ?
ICE
Fuels
Electrification
Efficiency improvements
55% BTE, Opposed piston
Low carbon fuels
Renewable fuels
Hybridization
Mild, full hybrid
Synthetic fuels
e-diesel
Alternate fuels
CNG, LPG
Ethanol
Fuel agnostic engines
Hybrid + green fuel
H2 ICE
Plug-in + Syn fuel
Volvo 7900 hybrid
Cummins 15L H2 ICE
Cummins fuel agnostic engines
ClearFlame Engine
Runs on ethanol
AchatesPower Opposed Piston engine
Detroit DD15, inline 6-cyl
2024 GHG compliant
ZEVs
Battery electrics
Fuel cell vehicles

## Slide 5: What problems are we are trying to solve in the transportation sector?
Cars (6%)
Shipping (2%)
Aviation (2%)
Buildings (16%)
Energy Supply (12%)
Industry (34%)
Freight vehicles (4%)
Ag., forestry and other land use (22%)
Global Greenhouse Gas emissions
Local Criteria Pollutants
We are nearing zero-impact emissions with upcoming regulatory steps (~ Euro 7/VII/EPA Tier 4/Low NOx/CN 7 …)
Source: https://www.epa.gov/air-trends/air-quality-cities-and-counties
US AQG today : 12 mg/m3
NAAQS 2023?
Source: IPCC 2022 https://www.ipcc.ch/report/ar6/wg3/

## Slide 6: Zero impact emissions will require a diverse set of technology solutions
Shift
Public transportation
Ride-sharing
Improve
Improved ICE efficiency
Light-weighting, aerodynamics etc.
Waste heat recovery
Predictive cruise control, platooning
Improved aftertreatment systems
Hybridization
Low carbon fuels
Cycling
Avoid
Geo-fencing
Electrification
Recycling
TECH MATURITY & CONSUMER ACCEPTANCE EXISTING INFRASTRUCTURE
Telecommuting
Rail & marine
Non-tailpipe emissions
H2-ICE
Fleet turnover
Urban planning

## Slide 7: Tailpipe criteria pollutant limits have reduced by >99% But we need to tackle real-world emission scenarios and high emitters
Particle Mass (g/bhp-h)
NOx (g/bhp-h)
99.8%
99.2%
US EPA heavy-duty diesel tailpipe standards
UC Riverside, SCAQMD https://doi.org/10.1016/j.scitotenv.2021.147224
NOx Emissions (g/bhp-hr)
Fleet emissions study of HD trucks and buses

## Slide 8: New low NOx regulations will require advancing ICEs
California Advanced Clean Trucks Regulation
Manufacturer ZEV* requirements as % of annual sales
* ZEVs defined as vehicles with zero tailpipe CO2 (BEV, FCEV)
California Low NOx Omnibus Rule
90% NOx emission reduction by MY2027
+ GHG Phase 2: CO2 25% ↓
But to BE or not to BE is no longer a question

## Slide 9
Technology for low NOx | Impact on NOx | Impact on CO2
Engine calibration | Lower engine out NOx | Little / none
Cylinder deactivation | Increased EO temp.  higher NOx conversion | Lower CO2
Closed crankcase | Lower NOx | Little / none
EGR pump | Better EGR authority | Improved pumping loop efficiency
SuperTurbo | Turbine bypass allows for early SCR warm-up | Engine heating can be offset
Opposed piston | Elevated temp. for early LO | Lower heat loss  lower CO2
Hybridization | Lower fuel consumption and emissions | Lower CO2, can offset EHC penalty
Increase SCR volume and catalyst loadings | Improved deNOx at high flow rates | Increased backpressure
Added cc-SCR w/ twin dosing | Early light-off and urea dosing possible | Increased backpressure
+ cc-DOC for NO2 | Increased fast SCR, slower light-off of cc-SCR | Increased backpressure, N2O
SCR on filter | Early light off of main (uF) SCR | Passive regen is complicated
Model based A/T controls, NH3 storage | DeNOx sensitive to level of pre-stored NH3 | Lower urea consumption
Late & multiple injections | Early light-off | Fuel penalty, increased HC/CO
Heated urea dosing | Early urea dosing, lower deposition risk | Some fuel penalty for heating
Catalyzed DEF solution | Low nitrate deposits, earlier dosing possible | Can eliminate heated dosing
Electrical heater / EHC | Early light-off | Need to manage fuel penalty
Diesel  CNG / LPG / Gasoline / H2-ICE / … | Lower engine out NOx and/or simpler A/T | Watch for CH4, H2 slip
Engine
+ Added SCR
+ Heat
Fuel

## Slide 10
US 2010 / Euro VI | Ref. | 
CA2027 / Euro VII (example configurations) | 1 2 3 4 | 
“Close-coupled” catalysts
Conventional system
2nd filter
Advanced technologies
Close-coupled SCR / DOC
Dual NH3 dosing
Active thermal management – electric heater, heated dosing etc.
SCR on filters
Ultra-high porosity substrates
…
*
*
*
*
*High filtration DPFs

## Slide 11: SWRI/CARB study shows pathway to 90% NOx reduction over useful life
Engine:
Cummins 2017 X15 6-cyl.
+ modified calibration
+ cylinder deactivation
SWRI, Vehicle Eff., Electrification & Emissions Conference, 2022
+ Improved mixing
After-treatment: Stage 3 Rework system
Ongoing work:
Testing of EPA Low N2O system
(hybrid Cu-Fe SCR catalyst)
Limits
Composite FTP
Corrected for crankcase emissions
Low Load Cycle
435K
600K
800K
435K
600K
800K
Aging (mileage)
20 – 35% margin
CO2 neutral
+ 1% penalty

## Slide 12
Some more technologies for further reductions in NOx, PM & CO2
Electric Heater
P < 7 kW
SWRI, Eaton, Corning Front. Mech. Eng 8:979771
doi: 10.3389/fmech.2022.979771
Electrically Heated Catalysts
Opposed piston engine
Fleet demonstration (Walmart)
890 Miles, > 3 days
Fuel economy 6.7 – 10.8 mpg
EPA 3-Bin Analysis of PEMS data
2031+ EPA proposed low limit met with >50% margin with aged catalysts
AchatesPower
32nd Real World Emissions Workshop, 2022
Ducted Fuel Injection
Four-duct DFI in optical engine @ 1200 rpm
NOx (g/kWh)
PM (g/kWh)
Sandia Natl. Lab
SAE Int. J. Engines 13(3):345-362, 2020

## Slide 13: Heavy duty engines serve diverse vehicle applications - Decarbonization will require a range of technology solutions
Regional haul tractor
~ 150 – 300 mi
Vocational ~ 50 – 150 mi
Transit bus ~ 150 mi
Long haul tractor ~ 300 - 500 mi
School bus ~ 100 mi
HD pickup / van ~ 50 – 75 mi
Total in-use ~ 23 million
Class 2b - 3
Class 3 - 7
Class 7 - 8
Class 7 - 8
Diesel
Gas
Other
Vehicle Class
Fuel type

## Slide 14: Vocational and regional delivery trucking is well poised for electrification Long-haul – need to address battery weight, charging time, infrastructure
> 1MWh battery pack needed for 500+ mile range
~ 2kWh/mi*
* 2kWh/mi 6 hrs overnight depot charging @ 100 kW for 300 mi
Case study
Fleet of 100 vocational EV trucks
4.5 MW peak power for immediate (end-of-shift) charging at 100 kW
78 – 86% substations can supply without any upgrades
Charging infrastructure will have to be developed
MW charging needed
NREL https://doi.org/10.1038/s41560-021-00855-0

## Slide 15: Battery raw materials could be a bottleneck for EVs in the next few years
Assumptions
Avg. battery pack sizes – 50 kWh in China, 60 kWh in Europe, 75 kWh in US
Vehicle sales flat in US and grow at 0.5% per year in all other regions
No separation of PHEV and BEV for simplicity
EV share (light-duty)
Battery demand for LD
Global capacity
+ HD, consumer electronics, energy storage …
Future needs for EU alone
Li : 36X Ni : 2X Co : 4X
“Metals for Clean Energy: Pathways to solving Europe’s raw materials challenge” Eurometaux, 2022
Mines cannot be built overnight
Recycling, new chemistries, smaller batteries…
Raw materials
20
Years for mine development
10
0

## Slide 16: H2 fuel cell vehicles are suited for long-haul (range, quick refueling) Need to address green H2 availability and infrastructure
H2 density (g/L) 16 27 36 40
We will need a lot of (green) H2 …
For ~ 0.5M long-haul trucks (25% of fleet today) running 350 mi per day
H2 annual requirement =
500,000 x 350mi x 365 day/yr x 0.144 kg-H2/mi
= ~ 9.2M tons
US total H2 demand today is 10M tons per year (NREL), almost all made from fossil fuels

## Slide 17: How much can we improve the internal combustion engine ?
Navistar, Book chapter in “Alternative Fuels and Advanced Vehicle Technologies for Improved Environmental Performance”, 2014
doi: 10.1533/9780857097422.2.225
Brake Thermal Efficiency (%)
1960
1970
1980
1990
2000
2010
2020
Year
ST 2 target
2009 baseline : 5.8 mpg
ST2 : 14 mpg (projected)
2019 production: 9 mpg
ST = SuperTruck (DOE program)
-35% fuel consumption
Daimler, 42nd Intl. Vienna Motor Symposium, 2021
Detroit DD15 : BTE 48%
3.4% lower fuel consumption
Meets 2024 GHG requirements
Compliance to 435,000 mi
NOx reduction by 60% on FTP

## Slide 18: Super-Truck II : 55% BTE & 2X freight efficiency
SuperTruck2
55% BTE
2X freight h
ENGINE
TRANSMISSION, ELECTRIFICATION
VEHICLE
Improved combustion
High CR + 0.3 – 0.8 BTE
Thermal barrier coatings - 1 % BSFC
Lower friction +0.5% BTE
Improved air handling
EGR pump (+0.9 BTE)
Miller cycle LIVC
High efficiency turbochargers
Waste heat recovery
~ +3 – 4.5% BTE
ORC with cyclopentane
Dual entry turbine
Improved after-treatment
Low DP design
cc-SCR, high cell density, thin wall
Eaton
48V mild hybridization, 7 – 15 kWh Li-ion battery. Electrification: HVAC, P-steering, coolant pumps, CAC, e-hoteling, etc.
Weight reduction
Navistar: ~ 4,000 lbs (trailer, frame)
Cummins: ~4,700 lbs (+ trailer solar panels)
PACCAR: 28%
Aerodynamics & tires
Aero drag reduced by ~ ~60% by NAV, Kenworth, Cummins, PACCAR
Rolling R : NAV 22% ↓, Cummins 33% ↓
Predictive cruise control
Navistar
Navistar
Model-based control
Cummins
https://www.energy.gov/eere/vehicles/annual-merit-review-presentations

## Slide 19: Vocational trucks: Combining high efficiency engine with mild-hybridization could reduce CO2 > 30% beyond model year 2027
ICCT White Paper, Nov 2021
Simulations using EPA GHG emission model (GEM)
+34% efficiency @ +$17,400
(All tech. have a < 2 yr. payback)
Class 6-7 vocational
7L engine, 49% BTE beyond MY2027
Fuel Consumption Reduction
FEV SAE 2021-01-0720 doi:10.4271/2021-01-0720
P3 mild hybrid for vocational truck
~ 24% reduced fuel consumption at reduced TCO

## Slide 20
H2 combustion – why ?!
Peak BTE 45% (similar to diesel) – but with 99% lower NOx
MAN, 42nd Intl. Vienna Motor Symposium, 2021
Westport Fuel Systems
43rd Intl. Vienna Motor Symposium, 2022
Biomethane
H2-ICE
40% blend
100% biomethane
Blue H2
80% Blue-20% green H2
Green H2
Carry over existing hardware from diesels
Well-to-wheel CO2 reduction vs. diesel
Utilization of existing hardware
Truck cost Diesel truck : €110K, H2 ICE : 1.3 – 1.4X, FCEV : 2.6 – 3.4X
Fuel cost Diesel : €1.5/liter, H2 : €6/kg
Driver cost : €60K/yr
Fuel
Driver
Truck
Service
Tires
TCO much lower than fuel cell vehicle
- Lower than diesel with higher fuel prices ?
H2
€8/kg
€4/kg
TCO parity needs significant H2 price reduction

## Slide 21: Low carbon fuels, fleet turnover will be needed to address decarbonization of existing fleet
Hybridization – 20% reduced FC
LD : 50% BEVs
HD : 15% ZEVs
High eff. ICE(3) : 30% reduced FC
US 2021 bio- and renewable diesel production(1)
(1) US EIA 2022 Annual Energy Outlook (2)Neste, 42nd Intl. Vienna Motor Symposium, 2021 (3)SuperTruck2: 55%BTE, mild hybrid, low RR tires, …
Announced capacity by 2025(2)
US Fuel Consumption (million barrels per day)
Scenario to 2030
Total ~ 21% of diesel use by 2025
Gasoline
Diesel
Jet fuel
NG
Ethanol
Assume 1.5X growth by 2030
Biden goal
3B gal/year of SAF by 2030

## Slide 22: We need to pursue all pathways for transport decarbonization
ICE
Fuels
Electrification
Efficiency improvements
55% BTE, Opposed piston
Low carbon fuels
Renewable fuels
Hybridization
Mild, full hybrid
Synthetic fuels
e-diesel
Alternate fuels
CNG, LPG
Ethanol
Fuel agnostic engines
Hybrid + green fuel
H2 ICE
Plug-in + Syn fuel
Volvo 7900 hybrid
Cummins 15L H2 ICE
Cummins fuel agnostic engines
ClearFlame Engine
Runs on ethanol
AchatesPower Opposed Piston engine
Detroit DD15, inline 6-cyl
2024 GHG compliant
ZEVs
Battery electrics
Fuel cell vehicles

## Slide 23: Thank you !
  Contact Info
joshia@corning.com
https://www.linkedin.com/in/joshiav/